Design 4 Space
TID on analog circuits
Cumulative effects on analog circuits
Francesco Poderico
www.neutronix.co.uk

---
Cumulative effect on Analoh Circuits
DC Biasing on CMOS amplifier
I = (μ Cox/2)(w/L)(Vg-Vt)2
    1. Before irradiation everything it's OK!
    1. After irradiation: DC point is shifted (I decreased, V modified)
Possible solutions:
Raise Vdd to restore the initial I (difficult solution)
Power consumption will increase!

---
Gain Bandwidth Product
GBW~ gm/Cout
gm =μCox(W/L)(Vg-Vt)= 2[(μCox/2)(W/L)Ibias].
When dose ↑ => μ ↓, Vtn ↑ => gm ↓ => GBW ↓
Possible corrections
Raise Vdd (obviously not easy)

---
Gain Bandwidth Product
As GBW will reduce => the phase margin will get smaller!
Possible solutions:
Have a large phase margin at beginning of project ( e.g. MF > 80⁰)
Use Miller effect to improve stability
Make a pole zero compensation
Use passive filter as much as possible

---
BJT Op Amp vs CMOS Op Amp
A mismatch on the Vt due to different dose radiation will cause a mismatch. For this reason is better to use in the differential stage BJT transistor
Do not use MOS diff AMP as comparator

---
Bipolar differential amplifier with “standard” mirror current
Better than MOS
As β ↓ the Rin ↓, gain ↓, BW↓ , Ic ↑

---
Bipolar differential amplifier with Wilson mirror current
Ic is more stable over radiation

---
Single stage amplifier with low input impedance
When you need a low impedance amplifier, it is better to drive the current from the collector.
How is possible to improve this circuit?

---
Better solution (for higher irradiation)
Consider to use a Wilson mirror