Radiation effects on CMOS
By Francesco Poderico
www.neutronix.co.uk

---
TID effects on digital CMOS circuits
As we are talking on digital circuits we are interested to understand how the speed (max. frequency) is effected and how the input and output threshold are effected as well.
Ron = 1/[μ Cox(W/L) (Vgs-Vt)] (as with the TID μ decrease, Vt increase => Ron increase)
Gm = μ Cox(W/L) (Vgs-Vt) ( therefore Gm decrease)
Vt increase (in module)
Leakage current between drain and source increase
Leakage current between adjacent MOS increase

---
Vtn on N-MOS and P-MOS, (note that Vtno decrease first and then increase)

---
A reduction of Vt on N-MOS may prevent MOS to switch off
Even the Id/Vgs is reduced prevent N-MOS to switch off as well

---
Vtn increase may prevent N-MOS from switch ON

---
The leakage current between D and S may prevent NMOS to switch OFF!
The leakage current between MOS ,may prevent the circuits to work correctly
Increase of static power

---
An increase (abs) of Vtp can prevent PMOS to switch ON

---
Question
On a LEO application do you prefer to use an NAND gate or an NOR gate ?

---
Solution : NAND gate

---
Timing issues
μ decrease => the rising and falling edge slows down. This may cause unwanted glitches for
not synchronous designs, and not meeting the timing for synchronous designs.
Solution => use only synchronous design if possible, add an high margin (e.g. 50%) for micro-space solutions!

---
Dynamic Power
As consequences of slower rising and falling edge, the dynamic power will increase!
Solution on micro-space product add a further margin of 20% on the power budget!